## Slide 1: St. Louis District Regulating Works RRAT
Notes: Introduce self.
Thank you for the opportunity to talk to you today about Low Water Reference Plane.

## Slide 2: Execution CG
Regulating Works (195-0)
  FY13 - $9.2M Budget plus $3.2M FY12 contract T for C’d ($12.5M total)
    $8.5M on Rock Removal Urgent & Compelling
    $1M on Rock Removal Phase 2
    $650k on 3 HSR Model Studies – (Mouth of the Meramec RM 165,
    Gray’s Point RM 53, Upper Browns Bar RM 29)
  FY14 - $31M Budget
    $18M on Rock Removal Phase 2
    $1.5M on SEIS
    $3.3M on Mosenthein Phase 4
    $2.9M on Dogtooth Bend Phase 5
    $1.6M on Eliza Point Phase 3
  FY15 - $9M Budget
    $5.5M on Grand Tower Phase 5
    $1.1M on SEIS

## Slide 3: FY 14 Workload CG – Mosenthein Phase 4 RM 175 - 171
We have seen a systematic increase in channel width over the last 10 years leading to additional maintenance dredging required.
Design includes the construction of Rootless Dike 173.4L and over 2 miles of revetment on the LDB from RM 175 – 173.8 and RM 172 – 171.
The total project cost is $3.3M
This project combines the Carondelet GP from 2013 and Mosenthein GP from 2011

## Slide 4: FY 14 Workload CG – Eliza Point Phase 3 RM 3 - 0
Address a repetitive dredge location and provide better channel alignment.
We have dredged over 300k cy since 2007 at a cost of $900k.
Design includes the construction of 4 weirs and 1 dike
The total project cost is $1.6M
The GP was approved at E-Action in 2012

## Slide 5: FY 14 Workload CG – Dogtooth Bend Phase 5 RM 35 - 30
Address a repetitive dredge location and provide better channel alignment.
We have dredged approximate 1.5M cy since 2006 at a cost of $2.8M.
Design includes the construction of 8 weirs and 1 dike
The total project cost is $2.9M
The GP was approved at E-Action in 2012

## Slide 6: FY 15 Workload CG – Grand Tower Phase 5 RM 75 - 66
- Address a repetitive dredge location and provide better channel alignment.
Design includes the construction of 2 chevrons, 3 weirs, 3 diverter dikes, 1 dike extension, and 2 dike shortenings.
The total project cost is estimated at $5.5M.
The GP was approved at E-Action in 2012.

## Slide 7
Why is Regulating Works Important

## Slide 8: Measuring Success
Dredging Reduction 1988/1989 – 2012/2013:
- Dredge volume decreased
- Channel maintained to deeper depths
- Channel maintenance cost was reduced
Increased channel reliability
Improved safety – Zero in channel groundings during low water period.

## Slide 9
Regulating Works Project Benefits vs. Costs

## Slide 10: Questions??